## Slide 1: Automated Aquarium Management System ‘AquaSafe’
Team “Aqua”
A.M.Mohamed Raheethus Alfer (2020/CSC/001)
K.M.Issath (2020/CSC/021)
I.Akash Ahamed (2020/CSC/019)
Department of Computer Science,
University of Jaffna

## Slide 2: Problem Definition
Conventional aquarium management systems require caretakers
Typical Maintenance activities are tedious
Required lots of man hours for maintenance
24 hours nurturing
Human errors can threaten aqua life

## Slide 3: Literature Review
Evolution of Aquarium Management
Glass aquarium invention in the 19th century
Technological advancements in filtration and monitoring
Interdisciplinary Approaches
Fish behavior and physiology models / Water chemistry and Microbiology models / IoT systems and data analytics models
Factors Affecting Fish Health
Water quality, pH, Temperature, Dissolved oxygen, electrical conductivity and total dissolved solids impact fish health

## Slide 4: Identified Solution
Robust pH level regulation
Automate the feeding system
Monitoring water condition and take relevant action
Alert user through local host
Control feeding system via local host

## Slide 5: Objectives
The Automated Aquarium Management System (AAMS) “AQUA SAFE” addresses the challenges faced by aquarium owners by automating essential tasks and optimizing the aquatic environment.
Key Objectives
pH level regulation
  Maintaining pH within the habitable range
Maintaining water level
  Ensuring an adequate water level through ultrasonic sensors
Monitoring water temperature
  Constantly monitoring water temperature for fish health
Feeding system
  Automating fish feeding to maintain a healthy ecosystem

## Slide 6: Components Used
Temperature Sensor - DS18B20
pH Sensor - E201
Ultrasonic Sensor - HC-SR04
Servo Motor - SG90
ESP32 Development Board
12V DC Pumps
Relays

## Slide 7: Solution Developed to Regulate pH
Components Used
  pH sensor(E201) - To measure the pH of the water
  Ultrasonic Sensor(HCSR04) - To measure the water level
  Relays - To on/off pump from ESP32
  Pumps - To fill/remove water
Proposed Method
  Measure the pH value and compare it with the threshold value
  If the pH is not in the predefined range, then turn on pump 1.
  Measure the water level.
  If the water level is lower than predefined value, turn off pump 1 and turn on pump 2.
  Measure the water level.
  If the water level is higher than predefined value, turn off pump 2.
  Repeat…

## Slide 8: Solution Developed to Feeding System
Components Used
  Servo Motor (SG90) - To open/close the feeding system lid.
Proposed Method
  Compare current time with last feeded time.
  Open the lid if the difference is greater than user defined value.
  Close the lid after 10s.
  Look for web command to open the feeder lid.
  Open feeder lid according to web command.

## Slide 9: Solution Developed to Measure Temperature
Components Used
  Temperature sensor(DS18B20) - To measure the temperature
Proposed Method
  Measure temperature of the water.
  Update the temperature value to a web server.
  Repeat…

## Slide 10: Control and MCU
MCU Used
  ESP32
Proposed Method
  Connect ESP32 to web.
  Look for web requests.
  Run the feeder system, water changing system and temperature sensor

## Slide 11: Program Logic

## Slide 12: Pin Configuration used with ESP32

## Slide 13: Program and the code
The program codes:
  Arduino (C++) code:
    Responsible for controlling the aquarium's sensors and actuators.

## Slide 14: Arduino program for the pH sensor (E-201)

## Slide 15: Arduino program for the Temperature sensor (DS18B20)

## Slide 16: Arduino Program for the Ultrasonic Sensor

## Slide 17: Arduino Program for Pumps (12V 2 Relay)

## Slide 18: Tinkercad link
We utilized Tinkercad components for the implementation of this project. However, since Tinkercad lacks certain components, we were unable to fully realize the project, using only the available components within the platform.
https://www.tinkercad.com/things/alnMJuT777o-raheethus-alfer/editel?sharecode=fga9-ktEqOrySDAYejhLyR8sOkAioy-UcgfjpWN-qkY

## Slide 19: Arduino Program for Full Code

## Slide 20: Pin Configuration used with Arduino

## Slide 21: Initializing Connection

## Slide 22: System Setup

## Slide 23: Future Improvements
Tank Refilling and Temperature
  Make the system sensitive to temperature changes
Feeding Mechanism
  Larger food particles, Liquid foods, Different types of food.
Food Level Indication
  Container food level indication
Water Reservoir Monitoring
  Monitoring the pH value and temperature of the reservoir
Enhance Feeding Functionality
  Database of feeding cycle for different fish breeds.
Inflow and Outflow Rates
  Using a pump with variable flow rate

## Slide 24: Thank You